## Slide 1: Decarbonizing German Road Freight Transport: Challenges and Measures
La décarbonation des mobilités vue du cœur de l’industrie automobile allemande - Mission d’étude en Allemagne
Özcan Deniz (German Aerospace Center, Institute of Vehicle Concepts)
Fraunhofer IAO Stuttgart, 28.06.2023

## Slide 2: Fields of activity of the German Aerospace Center
Aeronautics and aerospace
Energy and transport
Digitisation and security
Planning and implementation of German aerospace activities
Project executing agency for research funding

## Slide 3: PRESENT THROUGHOUT GERMANY
with more than 10,000 employees at 30 locations
Stade
Oldenburg
Hamburg
Trauen
Bremen
Hannover
Köln
Jülich
Rhein-Sieg-Kreis
Bonn
Stuttgart
Lampoldshausen
Zittau
Cottbus
Jena
Dresden
Augsburg
Ulm
Weilheim
Oberpfaffenhofen
Braunschweig
Neustrelitz
Cochstedt
Berlin
Göttingen
Bremerhaven
Brussels
Washington
Tokyo

## Slide 4: DLR Institute of Vehicle Concepts
Road transport
Road vehicles and digital systems
Transport management
Rail transport
Rail vehicles and infrastructure
Traffic management
Transport system
Transport development and impact
Urban mobility and development
Intermodal transport hubs
We think ahead on these topics
DLR = „Deutsches Zentrum für Luft- und Raumfahrt“

## Slide 5: Outline
Current challenges and opportunities for decarbonizing road freight transport
Scenario analysis of the market potential of alternative powertrains in commercial vehicles: Results of the BEniVer* research project
Insight into DLR´s vehicle concept “U-Shift”
*Begleitforschung Energiewende im Verkehr Accompanying research on the energy transition in transport)

## Slide 6: Development of the German Freight Transport
Chart: Transport performance of Freight Transport
| 1991 | 2020
Road | 254.7 | 484.4
Rail | 82.2 | 120.9
Waterway | 56 | 43.3
+65%
Chart: GHG Emissions of Freight Transport
| 1991 | 2020
Road | 38.67 | 56.67
Rail | 0.98 | 0.15
Waterway | 1.77 | 1.19
+40%
 Freight structure and logistics effects supported the growth of road freight vehicles over other transport modes
 Although vehicles have become more efficient, the absolute Co2 emissions in (road) freight transport have increased.
Chart: Efficiency of Freight Transport
| 1991 | 2020
Road | 151.8257 | 116.9901
Rail | 11.9221 | 1.2407
Waterway | 31.6071 | 27.4827
-23%
-13%
- 90%
 Road freight transport became more efficient through incremental technologies, rail freight transport through direct electrification
Source: DLR – Daten und Fakten: Güterverkehr

## Slide 7: Target of GHG emissions in the german transport sector (Climate Protection Act)
The Federal Climate Protection Act (KSG) sector target for 2030 is -48% vs. 2019, from 164 (2019) to 85 (2030) Mt CO2 eq.
Overall, GHG emissions are to be reduced by 65% from 1990 levels by 2030.
The goal is complete decarbonization or GHG neutrality by 2045.
Source: Klimaschutz im Verkehr | Umweltbundesamt
Reformed act of 2023: One common target for all sectors, no individual sector targets in 2030

## Slide 8: Moderate growth in freight transport performance Forecast of the Ministry of Transport
Freight transport will continue to increase. The highest growth is expected to be in road transport.
This results in a change in the modal split in favour of road freight transport, while rail and inland waterways are losing ground.
Source: PowerPoint-Präsentation (bund.de)
Increase in freight transport performance
change 2019-2051
Modal split
change 2019-2051

## Slide 9: Challenge to decarbonise road freight transport
Increased GHG emissions
Tight Targets for GHG emission reductions
The key challenge for the road freight sector is to significantly reduce GHG emissions with increasing transport demand
Increasing demand for road transport forecast
Notes: Energy efficiency is key measure to climate neutrality

## Slide 10: Current discourse in road freight transport in terms of climate change mitigation
Results of a workshop survey with international participants:
Technological options
Challenges
Source: IEA HEV-TCP TASK 41 Final Report

## Slide 11: Comparison of different powertrain options for heavy-duty trucks - Efficiency losses
 | E-Fuels with combustion engine | H2-combustion | Fuel Cell Electric | Battery Electric
Fuel production efficiency (well to tank) | 42% | 52% | 52% | 95%
vehicle efficiency (tank to wheel) | 40% | 38% | 52% | 74%
Overall efficiency (well to wheel) | 17% | 20% | 27% | 71%
Operated 40t trucks (250 days, daily 600km) | 11 | 13 | 18 | 46
Renewable Energy (3 MW wind turbine with 2.000 h/year = 6 Mio. kWh)
Source: JEC Well-to-Tank report v5 and DLR analysis

## Slide 12: Range anxiety for electric trucks in urban and regional transport mostly unfounded
Chart: Daily mileage of German trucks vs. Eletric range of current series or close to series model (BEV, FCEV)
| 3,5t | 7,5t | 12t | 18t | 26t | 40t | 3,5t | 7,5t | 12t | 18t | 26t | 40t | 3,5t | 7,5t | 12t | 18t | 26t | 40t | Nahbereich | Regionalbereich | Fernbereich
Volumen | 7900 | 38400 | 31400 | 29300 | 29200 | 46000 | 24400 | 55100 | 48500 | 71000 | 68200 | 95500 | 58900 | 84247 | 55400 | 98700 | 101500 | 168100
Hoch | 274 | 275 | 234 | 242 | 242 | 302 | 460 | 208 | 287 | 408 | 396 | 536 | 814 | 421.943 | 355 | 457 | 532 | 721
Niedrig | 9 | 53 | 42 | 45 | 38 | 64 | 35 | 208 | 113 | 177 | 166 | 230 | 71 | 368.07 | 155 | 317 | 321 | 472
Schließen | 141.545 | 153.364 | 133.444 | 131.5 | 132.2 | 179.833 | 244.1 | 208 | 198.6 | 284.818 | 267.273 | 370.143 | 453.2 | 386.176 | 244.667 | 379 | 408.6 | 602.25
Source: Special analysis of KBA statistics for commercial vehicles 2017
urban delivery
regional distribution
Long-haul transport
For urban derlivery and regional distribution, range of BEVs are suitable to meet daily mileages
FCEVs can cover the higher daily mileages and hard-to-plan routes – especially in long haul transport
increasing energy density of Li-Bat. and Megawatt charging systems enables higher daily ranges for BEVs

## Slide 13: Model availability widens for electric freight vehicles in all segments
Pick-up trucks
(N1 category)
Alke ATX 330E [2]
Clean Motion Re:volt [3]
Ford Transit (PHEV)[4]
Renault Master Z.E. Hydrogen [5]
BEV
FCEV
HEV
BEV
Mercedes-Benz eSprinter [6]
Fuso eCanter [9]
Quantron Q-Light FCEV 120 [8]
BEV
MAN eTGM [10]
Scania R450 Hybrid [12]
Volvo FE Electric [14]
Vans
(N1 category)
Light
Articulated Trucks
(N2 category)
Heavy
Articulated Trucks
(N3 category)
Semi-trailer Trucks
(N3 category)
Hyundai Xient Fuel Cell [13]
BEV
FCEV
HEV
Daimler eActros [11]
BEV
FCEV
HEV
Mercedes-Benz Atego FHEV (7]
series
series
not available
per order
e-converted
small series
series
SOP 2022
SOP 2024
small series
SOP 2022
small series
project vehicle
on sale in 2022
Notes: [2] https://www.alke.com/de-de/index.php
[3] https://cleanmotion.se/revolt/
[4] https://www.ford.de/service/ihre-mobilitaet/ask-ford/nutz-und-flottenfahrzeuge/nutzfahrzeuge-allgemein/ford-transit-custom-plug-in-hybrid-phev
[5] https://blog.renault.de/neues-von-renault-brennstoffzelle-fuer-kangoo-ze-master-ze/
[6] https://www.mercedes-benz.de/vans/de/sprinter/panel-van
[7] https://media.daimler.com/marsMediaSite/de/instance/ko/Atego-BlueTec-Hybrid-Hybrid-Lkw-beweisen-im-Praxiseinsatz-Alltagstauglichkeit-und-CO2-Kraftstoffeinsparpotenzial.xhtml?oid=9361912
[8] https://www.quantron.net/q-mobility/q-truck/q-light/
[9] https://www.electrive.net/2018/01/31/renault-trucks-bringt-2019-e-lkw-auf-den-markt/
[10] https://www.man.eu/de/de/lkw/alle-modelle/der-man-etgm/etgm.html
[11] https://www.mercedes-benz-trucks.com/de_DE/emobility/world/our-offer.html
[12] https://www.electrive.net/2018/12/06/ehighway-tests-bund-ordert-15-hybrid-lkw-bei-scania/
[13] https://www1.hyundai.news/de/unternehmen/hyundai-liefert-erste-xcient-fuel-cell-brennstoffzellen-lkw-aus/
[14] https://www.volvotrucks.de/de-de/trucks/trucks/volvo-fh/volvo-fh-electric.html

## Slide 14: The number of battery-electric series models will rise in the future
Source: IEA Global EV Outlook 2023
Source: IEA HEV-TCP TASK 41 Final Report
Current and announced zero emission commercial vehicle by type, release date and range, 2019-2024
2019-2024
2030
The three largest truck manufacturer groups in Europe aim to equi at
least every second sold trucks with an electric powertrain by 2030

## Slide 15: Comparison of the TCO structure of 40t semi-trailer tractor with different powertrains in long-distance transport
Today:
FCEV and BEV with high investment costs
Slight cost differences between H2-Storage-options for FCEV
After 2025:
TCO parity for FCEVs achieved from 2029 onwards
Investment cost will still be higher for BEV and FCEV than diesel trucks in 2030
Chart: 2020
| 350bar | 700bar | 350bar | 700bar | CH2 | LH2 | CH2 | LH2 | ICEV-D | H2-ICEV | FCEV | BEV
Anschaffung | 149632 | 251367.6437 | 259635.6476 | 209110.323 | 426318.542 | 432587.6179 | 394277.6337 | 377851.9583
Subventionen | 0 | 0 | 0 | 0 | -234268.4184 | -239518.4728 | -207435.674 | -193679.9481
Infrastruktur | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 8605.7965
Maut | 130438.4767 | 121899.1329 | 121899.1329 | 121899.1329 | 0 | 0 | 0 | 0
Kraftstoff | 344187.938 | 854144.6444 | 854144.6444 | 854144.6444 | 647640.922 | 647640.922 | 647640.922 | 323412.9566
Wartung | 115533.511 | 112869.9189 | 112869.9189 | 112869.9189 | 77787.5717 | 77787.5717 | 77787.5717 | 75123.9796
Steuern | 2673.0972 | 2673.0972 | 2673.0972 | 2673.0972 | 0 | 0 | 0 | 0
Reifen | 33205.8389 | 33205.8389 | 33205.8389 | 33205.8389 | 33205.8389 | 33205.8389 | 33205.8389 | 33205.8389
Versicherung | 36713.4189 | 36713.4189 | 36713.4189 | 36713.4189 | 36713.4189 | 36713.4189 | 36713.4189 | 36713.4189
Restwert | -29450.3498 | -49473.8093 | -51101.1056 | -41156.7857 | -40341.7573 | -40588.5313 | -39080.5084 | -38433.933
GESAMT | 782933.9308 | 1363399.8855 | 1370040.5931 | 1329459.5884 | 947056.1179 | 947828.3653 | 943109.2029 | 622800.0678
Source: Own DLR analysis

## Slide 16: Key factors to ramp-up zero-emission freight vehicles
Suitable policy framework
Availability of charging and refueling infrastructure
Reliable and efficient trucks
Purchase subsidies: 80% of the additional investment costs for vehicle and infrastructure procurement for BEVs and FCEVs are funded via the KSNI funding guideline (until 2026).
Road toll exemption for xEVs until 2026 and introduction of a CO2-based component in the toll calculation starting in 2024.
Vehicle tax exemption for xEVs until 2030
Special depreciation of xEV: 50% of the purchase in the first year

## Slide 17: Outline
Current challenges and opportunities for decarbonizing road freight transport
Scenario analysis of the market potential of alternative powertrains in commercial vehicles: Results of the BEniVer* research project
Insight into DLR´s vehicle concept “U-Shift”
*Begleitforschung Energiewende im Verkehr Accompanying research on the energy transition in transport)

## Slide 18: Scenario and market analysis software for simulating future commercial vehicle markets in Germany until 2050
Source: Özcan Deniz 2022 Development of a scenario model for the simulation of the technology diffusion in the commercial vehicle market in Germany, 35th International Electric Vehicle Symposium and Exhibition (EVS35) Oslo, Norway, June 11-15, 2022 https://elib.dlr.de/187389/1/EVS35-340138.pdf
Scenario assumption
Agent-based Modelling
Simulation of the market potential of alternative fuel and powertrain options in new vehicle market
Assessing the diffusion of energy and powertrain technologies in road traffic

## Slide 19: Scenario definition
Scenarios focusing on different technology options for the transport sector to meet climate targets.
Considered scenarios:
Reference Scenario
(GHG reduction of 80%)
Technology Scenarios (GHG reduction of 100% until 2045)
E-Fuels
Hydogen
Direct Electrification

## Slide 20: Main scenario assumptions to reach GHG-neutrality in 2045“scenario
  EU average CO2 emission targets for LDV 0 g/km in 2035 and for HDV 0 g/tkm in 2040
  CO2 price for fuels: 2030: 100 €/ton CO2; 2045: 300 €/ton CO2
  Forecast vehicle mileage: 2020: 83.5 billion veh-km; until 2030: +10%; until 2050 +20% compared to 2020
  Crudie oil price: 2020: 36€/bbl; 2030: 69€/bbl; 2050: 85€/bbl
 | E-Fuels | E-Mob | H2-Mobility
EU Fleet CO2 Emission regulation | Crediting of E-Fuel Blends in EU CO2 fleet emission regulation | - | -
Toll | - | Toll exemption for BEV and FCEV until 2035 | 
Vehicle tax | - | Tax exemption for BEV and FCEV until 2035 | 
Energy tax | Tax exemption for E-Fuels until 2035 | - | Tax exemption for H2 until 2035
Energy carrier price | Syn Diesel: 3,09 €/l (2030) | Electricity: 0,30 €/kWh (2030) | Hydrogen: 5,67 €/kg (2030)
Technology development | ICE (BTE 55% in 2030) | Lithium-Ion Bat system min price: 91€/kWh | Min. prices: Fuel Cell System 121€/kW, H2-Tank-System 322€/kg
Infrastructure availability | - | Roll-out Megawatt-Charger (800kW) until 2030 | Roll-out public H2-Station (CH2) until 2030

## Slide 21: Reference scenario Market potential for alternative powertrains
Status of new registrations 2020*:
96% ICE-D
2.7% xEV (9350 BEV, 947 HEV)
2020 - 2030:
Focus on incremental technology development of ICE-D
Parallel ramp-up of xEVs
First FCEV in heavy duty segment (simulation agents with higher mileage)
2030 - 2050:
Strong ramp-up of BEVs in light duty vehicle segment and after 2040 also in heavy duty segment
FCEV in particular for long-haul transport

## Slide 22: Reference scenario Development of mileage and energy consumption of fleet vehicles
Transport performance in billion vkm
Total mileage of road freight transport 97.7 vehicle kilometres in 2020
Share of electric mileage =13.2%
(target: 33%)
Energy consumption domestic LDV 261.8 PJ + HDV 445.6 PJ in 2017 = 707.4 PJ
- 29.9% compared to 2005
(Taget: -40%)
Final energy demand in Mio. PJ
Reduction target: About one third of the mileage in heavy road freight transport should be covered electric or on the basis of electricity-based fuels by 2030.
Germany has committed to reducing final energy consumption in transport by 10 % by 2020 and by 40 % by 2050 compared to 2005.

## Slide 23: Sceanrio comparison Market potential of alternative powertrains
BEV as dominate powertrain post-2030 – especially for Light Duty Vehicles
Market potential of Fuel Cell Electric Heavy Duty Vehicles in long haul operation
Limited adoption of conventional vehicles fueled by E-fuels
Ref-Scenario

## Slide 24: Sceanrio comparison Development of the final energy demand
Increasing share of BEVs while total mileage increases, reduce final energy demand in all scenarios
The “Energy Efficiency Target for 2050” is met at closest by the Electric Mobility scenario
- 35,9%*
- 33,7%*
- 29,82%*
Peak demand for electricity in 2050: approx. 55 TWh
Peak H2 demand in 2045: approx. 48 TWh
Reducing final energy consumption by 40%

## Slide 25: Conclusion of the scenario analysis
Direct electrification of trucks (BEV) shows the highesr market potential in all vehicle segments
  Essential for the market ramp-up of BEVs are the current funding of the purchase price, toll exemption and decreasing production costs for lithium-ion batteries
Fuel cell electric trucks shows market potential for heavy long-distance applications where range and payload of BEVs do not meet user requirements
  However, the market volume of these segments are low, which is why economies of scale for fuel cells are lower too
The Ram-up of a megawatt charging and hydrogen filling stations (on long-distance roads) are simultaneously necessary with the electric vehicle adoption
CNG/LNG show low market potential - simultaneous, multiple investments in R&D and infrastructure not beneficial
E-fuels as an blend in diesel fuel may be necessary for decarbonisation of fleet vehicle. The Potential depends on dynamics of fleet renewal - rapid, early market penetration of BEVs reduces the potential
Limitation of the scenario analysis:
Predominantly technological potentials modelled
Shift potentials (to rail) or structural change in the industry/logistics associated with lower mileage

## Slide 26: Outline
Current challenges and opportunities for decarbonizing road freight transport
Scenario analysis of the market potential of alternative powertrains in commercial vehicles: Results of the BEniVer* research project
Insight into DLR´s vehicle concept “U-Shift”
*Begleitforschung Energiewende im Verkehr Accompanying research on the energy transition in transport)

## Slide 27: U-Shift - vehicle concept at a glance
Driveboard
Personal capsule
Freight capsule
Flexible transport of people or goods
Automated drive board with electric drive train
Automatic capsule change without operating personnel and without special infrastructure
Passenger capsule for public transport, 8 seats, integrated ramp for wheelchair/pram etc.
Goods capsule for 3 - 4 Euro pallets with a payload of 2,000 kg
A Major Shift
U-Shift project: Modularity leads to efficiency – and defines completely new possibilities in the transport of goods and people in an urban context.

## Slide 28: Characteristics of Driveboard + Capsules
„On-the-Road“Modularisation
Driveboard:
Standardised
Electrically driven
Integrated lifting function
High capacity, efficient use
Automated operation
Capsules:
Large number of variants for a wide range of applications (people / goods / service)
Individualised
Flexible, can be used as needed
"Simple", light, cost-effective
City logistics:
CEP, last mile,
trade, craft, general cargo, ...
PUBLIC TRANSPORT:
Peoplemover, neighbourhood bus, large-capacity taxi, ...

## Slide 29
Visiting the U-Shift
Bundesgartenschau 2023
Mannheim (Spinelli)
Fr., 14. Apr. 2023 – So., 8. Okt. 2023

## Slide 30: DLR U-Shift exhibition contribution
DLR U-Shift Pavillon
Nordeingang
Seilbahn vom anderen Neckarufer
West- eingang
DLR Pavillon
Südeingang
U-Shift Fahrzeuge
Strecken-Optionen
Notes: Auf Buga sind 2 Driveboards: „U-Shift I“ + „U-Shift IV“
Auf Buga sind zwei Kapseln: Kapsel „U-Shift I“ + „U-Shift IV
Auf Buga ist eine „Multi-Use-Plattform“

## Slide 31: Tip for the way back from the BUGA - in case of departure by train
Use the cable car and leave the Luisenpark at the main entrance, from there to the main station.

## Slide 32: U-Shift Video

## Slide 33
Any Questions?
Özcan Deniz
German Aerospace Center
Institute of Vehicle Concepts | Vehicle Systems and Technology Assessment
Stuttgart, Germany
Telephone +49 711 6862-8637 | oezcan.deniz@dlr.de